Robotics First Project

Descriptions of the files
We preferred to use a multi-package approach, making the project clearer and more readable. Each node therefore has its own package.

Briefly descriptions of the packages:

1. Sincronizzatore: subscribes to the four topics of the motor speed bag, synchronises them with the "exact time" policy and publishes them on a custom message we have created, called "WheelSpeeds", consisting of a header and four floats. It publishes this custom message on the topic called “vettore_motori”.
2. Baseline: contains two nodes: gen_baseline and gen_baseline_gtpose. The gen_baseline node calculates the gear ratio and the baseline by subscribing to scout_odom and vector_engines, averaging over 10000 values (almost the entirety of the bag, so we believe the average approximates the exact value very well) and with due consideration (see code), the results are as follows: gear ratio: 1:38.218040; baseline: 1.012144.
  The gen_baseline_gtpose node proceeds in the same way but by subscribing to gtpose instead of scout_odom, the results are:
3. Generazione: subscribes to vettore_motori and using the gear ratio and the appareant baseline calculates the six linear and angular velocities using formulas from Differential Drive theory and posts the results on the topic "twist_stamped" as a geometry_msgs of type TwistStamped.
4. Integrazione: is the main package and performs four functions:
  - the "integrator" node subscribes to the twist_stamped topic and calculates the pose at each time instant by integrating according to the Euler and Runge-Kutta methods selected via Dynamic Reconfigure and publishes the results in two different topics: integration_odom of type nav_msgs::Odometry and on our custom message odom_and_method which contains both the odometry and a string specifying the integration method (request no. 4).
  - Inside the package we have implemented Dynamic Reconfigure via the Python file methods.cfg inside the "cfg" folder. In this file the enum parameter is specified which can take values "euler(0)" and "rk(1)" depending on the selected method, these values are taken from the integrator node via callback_dyn. The default integration method is Euler.
  - The integrator node plays the role of a server with two services: ResetZero and GivenPose (see the description of the "service" package).
  - finally, we have specified the initial values of x,y and theta as initialized parameters in the launcher.
5. Rviz_publishing: contains two nodes: rviz_publisher and rviz_publisher_scoutodom, which define the links between the frame_id "world" and the child_frames "integration_odom" (our odometry) and "odom" (scout_odom's odometry). Thanks to these transformations we can plot our odometry and scout_odom's odometry on rviz referring both to the same static frame "world". The rviz configuration is saved in the "config" folder.
6. Service: contains in the srv folder the files ResetZero and GivenPose, which specify the parameters with which the services are called, respectively, the first to reset the odometry in the origin and the second to set it to the coordinates of your choice. Everything is done through the "Client" node which calls the two services of the integrator node (which plays the role of server).